SPI and V4L2
Jyothi A.

---
Contents
SPI
Introduction
Separate slave line
Single slave line
Programming in SPI
Advantages of SPI
Disadvantages of SPI

---
 Cont...
V4L2
    - Introduction
    - Data Structures
    - Input / Output
    - Capturing Video

---
Serial Peripheral Interface
(SPI)

---
 Introduction
SPI is an interface bus commonly used to send data between microcontrollers and small peripherals such as
- shift registers
- sensors
- SD cards
SPI developed by motorola to provide full duplex synchronous serial communication.

---
Cont...
SPI has synchronous solution to receive data.

---
Cont...
- SPI has four pins:
  - SCK / CLK : generates clock signal.
  - MOSI : data sent from master to slave, Master Out Slave In
  - MISO : data sent from slave to master, Master In Slave Out
  - SS : used to select the required slave

---
Cont...

---
Cont...
- Multiple slaves : 2 ways
  - separate slave lines
  - single SS line (daisy chain configuration)

---
 Separate Slave Lines

---
 Single SS line

---
Cont...
- SPI transfer example
  - when master wants to initiate transfer, it must pull SS signal low for the slave it wants to communicate with
  - once SS signal is low, that slave will be listening on the bus
  - master is free to start sending data

---
Cont...
- There are 4 different types of SCK signal. The four modes are categorized into two:
  - CPOL (clock polarity) : value low/high will decide the idle state of bus
  - CPHA (clock phase) : sampling of data during rising or falling edge of the clock

---
Cont...
SPI mode	Clock Polarity / (CPOL)	Clock Phase / (CPHA)	Clock Edge
0	0	0	1
1	0	1	0
2	1	0	1
3	1	1	0

---
 Programming in SPI
- The programming interface is structured around two kinds of driver
  - Controller driver
  - Protocol driver

---
 Cont...
struct spi_master{
  struct device dev;
  u16 num_chipselect;
  size_t (*)(struct spi_device *spi) max_transfer_size;
  int (*)(struct spi_device *spi,struct spi_message *mesg) transfer;
  void (*)(struct spi_device *spi) cleanup;
  …
  ...
};

---
 Cont...
struct spi_device{
  struct device dev;
  struct spi_master *master;
  u8 chip_select;
  void *controller_state;
  void *controller_data;
  ...
  ...
};

---
 Cont...
struct spi_board_info {
  const void * platform_data;
  void * controller_data;
  u16 chip_select;
  u16 mode;
  ...
  ...
- };

---
 Cont...
struct spi_driver {
  const struct spi_device_id * id_table;
  int (* probe) (struct spi_device *spi);
  int (* remove) (struct spi_device *spi);
  void (* shutdown) (struct spi_device *spi);
  struct device_driver driver;
};

---
 Cont...
struct spi_message {
  struct spi_device * spi;
unsigned frame_length;
unsigned actual_length;
int status;
...
  ...
};

---
 Cont...
struct spi_transfer {
  unsigned tx_nbits:3;
  unsigned rx_nbits:3;
  u8 bits_per_word;
  u16 delay_usecs;
  u32 speed_hz;
  ...
  ...
};

---
Advantages of SPI
- It’s faster than asynchronous serial
- The receive hardware can be a simple shift register
- It supports multiple slaves

---
  Disadvantages of SPI
- It requires more signal lines (wires) than other communications methods
- The communications must be well-defined in advance
- The master must control all communications
- It usually requires separate SS lines to each slave, which can be problematic if numerous slaves are needed

---
Video 4 Linux 2
(V4L2)

---
  Introduction
- V4L is a collection of device drivers and an API for supporting real time video capture on Linux system.
- Programming a V4L2 device consists of below steps:
  - Opening the device - open()
  - Changing device properties, selecting a video and audio output, video standard, picture brightness - ioctl()
  - Negotiating a data format - ioctl()
  - Negotiating an input/output method - ioctl()
  - The actual input/output method – ioctl()
  - Closing the device - close()

---
Cont...
- V4L2 drivers are implemented as kernel modules.
- Driver modules plug into the “video-dev” kernel module
- Each driver has major number – 81, minor number ranges from 0 – 255
- The module options to select minor numbers are named after the device special file with a "_nr" suffix
  Ex: "video_nr" for /dev/video video capture devices

---
 Data Structures
struct v4l2_capability
{
        __u32 capabilities; /* Device capabilities */
        ...
} cap ;

---
Cont...
struct v4l2_format
{
        enum v4l2_buf_type type;
        union
        {
        struct v4l2_pix_format pix;
        ...
        } fmt;
} fmt ;

---
 Input/Output
- Read / Write
- Streaming
  - Memory mapping : Map buffers in device memory into
    the application’s address space
  - User Pointer : Buffers are allocated by the application itself. The driver must be switched into user pointer I/O mode with desired buffer type

---
 Capturing Video
open_device( )
fd = open ( “/dev/video0”, O_RDONLY ) ;
init_device ( )
ioctl ( fd ,VIDIOC_QUERYCAP, &cap ) ;
/* Select video input, video standard and format */
ioctl ( fd, VIDIOC_ENUM_FMT, &fmt ) ;
start_capturing ( )
 ioctl ( fd, VIDIOC_STREAMON, &type ) ;

---
Cont...
read_frame ( )
ioctl ( fd, VIDIOC_DQBUF, &buf ) ;
ioctl ( fd, VIDIOC_QBUF, &buf ) ;
process_image ( )
/* Application Dependent */

---
Cont...
stop_capturing ( )
 ioctl ( fd, VIDIOC_STREAMOFF, &type ) ;
uninit_device( )
free ( ) ;
close_device ( )
close ( fd ) ;